## Slide 1: You want me to test for what?
Laboratory Testing During a Pandemic
J. Eric Stanford, MHA, MLS(ASCP)cm
Laboratory Manager – Vanderbilt University Medical Center

## Slide 2: Objectives
What is an Emergency Use Authorization (EUA) and what is the mechanism for submission?
What role do laboratories play in health care during a global pandemic?
How do laboratories develop testing for novel biological agents under an EUA?

## Slide 3: COVID-19
December 2019 – Wuhan, China
SARS-CoV-2 – Sudden Acute Respiratory Syndrome, Coronavirus 2
Coronaviruses – respiratory virus that ranges from mild to severe
Corona = Crown – virus utilizes spike protein to bind with cells
COVID-19 is the 7th Coronavirus to infect humans – 3rd animal crossover (Binnicker, 2020)
(COVID-19 Digital Press Kit, 2022)
(COVID-19 and Your Health, 2020)

## Slide 4: COVID-19
“Transmission electron microscopic image of an isolate from the first U.S. case of COVID-19, formerly known as 2019-nCoV. The spherical viral particles, colorized blue, contain cross-sections through the viral genome, seen as black dots.” (Bullock & Tamin, 2020)

## Slide 5: Objectives
What is an Emergency Use Authorization (EUA) and what is the mechanism for submission?

## Slide 6: What is an Emergency Use Authorization?
First authorized in 2004
  Bioterrorism/Anthrax
  H1N1
  Ebola
  Avian Flu
  Middle Eastern Respiratory Syndrome (MERS)
  COVID-19
(Macmillan, 2022)

## Slide 7: What is an Emergency Use Authorization?
EUA is an avenue for products to reach the market/consumer/patient more quickly in a public health emergency
Must be lacking in “adequate, approved, available alternatives…and when the known and potential benefits outweigh the potential risks” (Macmillan, 2022).

## Slide 8: What is an Emergency Use Authorization?
Full FDA approval can take years through a very extensive process – the EUA shortens this timeline (without sacrificing rigorous standards) (Macmillan, 2022)
EUA can be retracted at any time when new data becomes available (Macmillan, 2022)

## Slide 9: What is an Emergency Use Authorization?
Public Health Emergency Declared
A formal HHS declaration of a public health emergency
Pre-EUA Submission Meeting
Helps facilitate submission process
Submission
Review by FDA
Approve/Reject
Termination
FDA issues ruling
EUA ends when the emergency is over, or EUA is revoked

## Slide 10: What is an Emergency Use Authorization?
Two main differences between full FDA approval and EUA
  Shortened window of patient follow-up, such as vaccines and medical devices
  Less data needed concerning processes, inspections, and facilities – less data needed for review
Full approval requires submission of a Biologics License Application (BLA)
  Follows a set of rigorous development and clinical trial steps
(Macmillan, 2022)

## Slide 11: What is an Emergency Use Authorization?
EUA follows the same basic process
  Safety board – established by the manufacturer to review unblinded trial data during the trial to monitor for safety
  FDA Center for Biologics Evaluation and Research
  Public Meeting to review data
EUA can be terminated, either by the end of the emergency declaration or when performance characteristics are deemed unsuitable (Robinson et al., 2021)
(Macmillan, 2022)

## Slide 12: What is an Emergency Use Authorization?
Full approval of a vaccine, for example, has a “median clinical development period…[of] just over 8 years” and “median FDA review period of about a year” (Macmillan, 2022).

## Slide 13: What is an Emergency Use Authorization?
Pfizer vaccine developed in six months, with EUA less than a month later – full approval 8 months later
  In this case, intense focus and resource allocation was dedicated to the effort, resulting in a faster development time
  The advisory boards recommended submission of EUA early in the trial based upon the clinical trial data that showed significant benefit and limited risk
(Macmillan, 2022)

## Slide 14: Objectives
How do laboratories develop testing for novel biological agents under an EUA?

## Slide 15: Testing Timeline
Jan 27
FDA describes COVID-19 EUA strategy
Feb 4th
CDC issued EUA for their 2019-nCoV RT-PCR
Feb 6
CDC ships test to state public health labs
March 12
Roche issued EUA
First Commercial Test
March 18
Abbott launches rapid molecular test
April 21
First at-home test authorized
May 8
First antigen test authorized
July 18
EUA for sample pooling
July 31
First antibody test authorized
Aug 6
Second antibody test revoked
Jan 10
Genome sequenced
Jan 17
First diagnostic test developed in Germany
Jan 24
CDC releases guidance on US developed test
Feb 12
CDC announces error in test
Feb 29
FDA allows high complexity labs to develop test
March 9th
VUMC in-house test approved

## Slide 16: EUA and LDTs
To understand the EUA process, we must understand the LDT process
Laboratory Developed Tests include any in vitro diagnostic test that the performance characteristics have not been evaluated by the FDA and were evaluated/developed through clinical verification within the laboratory
(Adashi & Cohen, (2022)

## Slide 17: EUA and LDTs
FDA has made attempts to more strongly regulate LDTs but has thus far been problematic (Robinson et al., 2021)
Feb 29, 2020 FDA enforced regulatory oversight of LDTs
August 19th, 2020 HHS announced FDA would not review EUA applications
Nov 15, 2021 HHS reversed policy that removed FDA authority to regulate LDTs
(Adashi & Cohen, (2022)

## Slide 18: EUA and LDTs
FDA definition
(“Information for Laboratories Implementing IVD Tests Under EUA,” 2021)

## Slide 19: EUA and LDTs
LDT
  “must use only in-house materials, general purpose reagents (GPRs), and analyte specific reagents (ASRs)”
  GPR – “chemical reagents that might commonly be used in a laboratory, such as a pH buffer”
  (Robinson et al., 2021)

## Slide 20: EUA and LDTs
LDT
  ASR – “antibodies, both polyclonal and monoclonal, specific receptor proteins, ligands, nucleic acid sequences, and similar reagents which, through specific binding or chemical reactions with substances in a specimen, are intended for use in a diagnostic application for identification and quantification of an individual chemical substance or ligand in biological specimens” (21 CFR 864.4020)”
  Only used within a single laboratory under a single CLIA license
  (Robinson et al., 2021)

## Slide 21: EUA and LDTs
LDT
  LDTs can only be performed in laboratories “certified to conduct high-complexity testing” (Adashi & Cohen, 2022).
  Cannot be used in direct-to-consumer testing (Adashi & Cohen, 2022; Robinson et al., 2021)
(Waters, n.d.)

## Slide 22: EUA and LDTs
LDT
  LDTs are not limited to EUA situations – they fill a gap in commercially available testing protocols
    Genetic
    Molecular
    Toxicology
(Waters, n.d.)

## Slide 23: LDT vs FDA-Modified
FDA-modified test
  Off-label use of an FDA approved assay/method
  Example:
    Utilizing a specimen type that was not approved for use in the package insert
    Alter the process/protocol steps, such as extraction steps
  Not limited to a single laboratory

## Slide 24: LDT vs FDA-Modified
LDT
  A test kit does not exist
  A method is not available
  Could utilize existing equipment (such as an HPLC-MSMS)
  Used to test where a commercial kit does not exist or does not meet the needs of the laboratory
  Limited to a single laboratory/CLIA license

## Slide 25: Validation vs. Verification
Validation
  Usually performed by manufacturers for FDA review
  “provides proof that a method is suitable for its intended use and that it fulfills the necessary quality requirements” (Pum, 2019)

## Slide 26: Validation vs. Verification
Verification
  Usually performed by the laboratory on an FDA approved method/platform/assay
  Used to “verify method precision, accuracy, detection limit and measurement range, as well as…method comparison experiment and to verify the reference interval of the new method” (Pum, 2019)
  “confirmation that the laboratory using the test can replicate the manufacturer’s performance claim when the test is used according to the package insert” (Burd, 2010).

## Slide 27: LDTs
  Requires extra steps to validate the LDT
    Analytical Specificity
    Analytical Sensitivity
    Interference
    Limit of detection
    Cross-reactivity
    Development of calibration and quality control protocols
    Specimen type
    Extraction methods
    Protocol development
    Possible IRB approval needed
(Burd, 2010)

## Slide 28: LDTs
Disclaimer
  Laboratories are required to notify clinicians that a test is laboratory developed
  Must append the following to results generated using the LDT
    “This test was developed and its performance characteristics determined by [laboratory name]. It has not been cleared or approved by the U.S. Food and Drug Administration,”
(Burd, 2010)

## Slide 29: LDTs
Disclaimer
  College of American Pathologists recommend additional information:
    “The FDA has determined that such clearance or approval is not necessary. This test is used for clinical purposes. It should not be regarded as investigational or for research. This laboratory is certified under the Clinical Laboratory Improvement Amendments of 1988 (CLIA-88) as qualified to perform high complexity clinical laboratory testing”
    Eliminates confusion that a test is not approved rather than it did not require review
(Burd, 2010)

## Slide 30: LDTs
All of this takes time…

## Slide 31: LDTs in an emergency…
For an emergency situation, the number and types of studies that must be done in a validation are much less stringent
A complex precision study can take 20 days or more – precision in an EUA situation could be say, 5 days

## Slide 32: LDTs in an emergency…
Pre-market review of a commercially developed test can be waived in an EUA situation
For COVID-19, the FDA provided guidance to laboratories authorizing use of LDT testing for clinical use before EUA when all validation/verification criteria have been completed satisfactorily and the FDA has been notified (Sarata, 2021)

## Slide 33: LDTs in an emergency…
With the initial roll-out of the CDC assay, significant problems were detected both by the CDC and other laboratories performing the test
The test kit included molecular probes and primers, one of which returned “inconclusive results” (Sarata, 2021)

## Slide 34: LDTs in an emergency…
A test kit was already being distributed in other parts of the world by the World Health Organization (WHO)
The decision to develop its own test rather than use the WHO kit, and subsequent issues with the CDC test kit, severely hampered US efforts to combat the early disease progression (Sarata, 2021).

## Slide 35: Objectives
What role do laboratories play in health care during a global pandemic?

## Slide 36: Public and Private Laboratories
Early stages of testing in the US limited testing to CDC laboratories
It was subsequently expanded to state public health laboratories
This was done to control surveillance and reporting
(Binnicker, 2020)

## Slide 37: Public and Private Laboratories
It soon became clear that the testing capabilities of federal and state laboratories was woefully under-prepared and unable to keep up with testing demand
Shipping samples to these labs takes time – valuable time that can delay treatment
Physicians and front-line testing laboratories need the ability to perform testing
(Binnicker, 2020)

## Slide 38: Public Health Infrastructure
CDC/WHO
Vendors
Labs
Binnicker (2020) proposes a structure that disseminates testing capabilities to the front lines as quickly as possible
  Agencies such as WHO and CDC have the best proximity to “develop new diagnostic tests rapidly”
  Vendors should then be engaged to mass produce the protocol
  Distribute to laboratories

## Slide 39: Public Health Infrastructure
When we are able to test sooner, and more broadly, resources such as personal protective equipment can be more appropriately utilized (Lieberman et al., 2020)
The next pandemic is just around the corner – preparation is key (Khanna et al., 2020)
Strategies need to be developed to ensure resource availability and public health response is appropriate and timely, i.e., surveillance and reporting structures (Khanna et al., 2020).

## Slide 40: Clinical Laboratories
Clinical laboratories must be able to flex testing platforms and personnel to meet new demands for testing
Laboratory budgets are already extremely tight, and limited funding hinders this adaptability
Likewise, hospital resource allocation is another area of concern
  Personnel
  Equipment
  Facilities

## Slide 41: Clinical Laboratories
Ebola taught us that we were not prepared for testing in an isolation scenario
COVID-19 taught us that laboratories are not prepared for overwhelming testing demands, especially at the state and federal level
Staffing plans are not flexible enough to meet fast-changing scenarios due to training and competency needs
Testing and treatment rationing is a necessary response

## Slide 42: Global Supply Chain
Perhaps one of the greatest discoveries of the effects of a global, modern pandemic is the affect it has had on global supply chain services
Even where resources existed, getting supplies from point A to point B proved challenging
More importantly, the stark differences between wealthy and poor nations was severely highlighted (Khoo & Lantos, 2020).

## Slide 43: Contact Information
Eric Stanford
Email: eric.Stanford@vumc.org
Vanderbilt University Medical Center

## Slide 44: References
Adashi, E. Y., & Cohen, I. G. (2022). SARS-CoV-2 Laboratory-Developed Tests: Integrity Restored. JAMA. https://doi.org/10.1001/jama.2022.3382
Binnicker, M. J. (2020). Emergence of a Novel Coronavirus Disease (COVID-19) and the Importance of Diagnostic Testing: Why Partnership between Clinical Laboratories, Public Health Agencies, and Industry Is Essential to Control the Outbreak. Clinical Chemistry, 66(5), 664–666. https://doi.org/10.1093/clinchem/hvaa071
Bullock, H., & Tamin, A. (2020). Coronavirus Image 23354. Details - Public Health Image Library(PHIL). https://phil.cdc.gov/Details.aspx?pid=23354
Burd, E. M. (2010). Validation of Laboratory-Developed Molecular Assays for Infectious Diseases. Clinical Microbiology Reviews, 23(3), 550–576. https://doi.org/10.1128/CMR.00074-09
CDC. (2020, February 11). COVID-19 and Your Health. Centers for Disease Control and Prevention. https://www.cdc.gov/coronavirus/2019-ncov/your-health/about-covid-19/basics-covid-19.html
Commissioner, O. of the. (2022). Emergency Use Authorization. FDA. https://www.fda.gov/emergency-preparedness-and-response/mcm-legal-regulatory-and-policy-framework/emergency-use-authorization
COVID-19 and Your Health. (2020, February 11). Centers for Disease Control and Prevention. https://www.cdc.gov/coronavirus/2019-ncov/your-health/about-covid-19/basics-covid-19.html
COVID-19 Digital Press Kit. (2022, February 3). Centers for Disease Control and Prevention. https://www.cdc.gov/media/dpk/diseases-and-conditions/coronavirus/coronavirus-2020.html

## Slide 45: References
Emergency Use Authorization for Vaccines Explained. (2020). FDA. https://www.fda.gov/vaccines-blood-biologics/vaccines/emergency-use-authorization-vaccines-explained
Information for Laboratories Implementing IVD Tests Under EUA. (2021). FDA. https://www.fda.gov/emergency-preparedness-and-response/mcm-legal-regulatory-and-policy-framework/information-laboratories-implementing-ivd-tests-under-eua
Khanna, R. C., Cicinelli, M. V., Gilbert, S. S., Honavar, S. G., & Murthy, G. V. S. (2020). COVID-19 pandemic: Lessons learned and future directions. Indian Journal of Ophthalmology, 68(5), 703–710. https://doi.org/10.4103/ijo.IJO_843_20
Khoo, E. J., & Lantos, J. D. (2020). Lessons learned from the COVID‐19 pandemic. Acta Paediatrica (Oslo, Norway : 1992), 10.1111/apa.15307. https://doi.org/10.1111/apa.15307
Lieberman, J. A., Pepper, G., Naccache, S. N., Huang, M.-L., Jerome, K. R., & Greninger, A. L. (2020). Comparison of Commercially Available and Laboratory-Developed Assays for In Vitro Detection of SARS-CoV-2 in Clinical Laboratories. Journal of Clinical Microbiology, 58(8), e00821-20. https://doi.org/10.1128/JCM.00821-20
Macmillan, C. (2022, March 7). Emergency Use Authorization Vs. Full FDA Approval: What’s the Difference? Yale Medicine. https://www.yalemedicine.org/news/what-does-eua-mean
Moshkovits, I., & Shepshelovich, D. (2022). Emergency Use Authorizations of COVID-19–Related Medical Products. JAMA Internal Medicine, 182(2), 228–229. https://doi.org/10.1001/jamainternmed.2021.7257
Pum, J. (2019). Chapter Six—A practical guide to validation and verification of analytical methods in the clinical laboratory. In G. S. Makowski (Ed.), Advances in Clinical Chemistry (Vol. 90, pp. 215–281). Elsevier. https://doi.org/10.1016/bs.acc.2019.01.006

## Slide 46: References
Robinson, S., Carter, A., & Brindley, Da. (2021, August 30). The changing regulatory landscape for laboratory developed tests. https://www.raps.org/news-and-articles/news-articles/2021/8/the-changing-regulatory-landscape-for-laboratory-d
Sarata, A. K. (2021). Early Development and Regulation of Diagnostic Testing for COVID-19: Frequently Asked Questions. 14.
Waters. (n.d.). How Does High Performance Liquid Chromatography Work? | Waters. Retrieved March 29, 2022, from https://www.waters.com/waters/en_US/How-Does-High-Performance-Liquid-Chromatography-Work%3F/nav.htm?cid=10049055&locale=en_US